جامعة آل البيت

دائرة العطاءات المركزية				                                 		              Central Committee for Tender

مواصفات العطاء رقم (7/2017)

صيانة الخوادم الحاسوبية الرئيسية

- IBM Power 550 ,Qty=2

| Description |
| --- |
| Architecture | Rack Up to 8 – Cores RISC Server ( over four Processor ) |
| CPU | 64 bit RISC Based Processor & up to date Architecture |
|  | Two x Dual core 3.5 GHz POWER 6 Processor Card up to 8-Cores support fully symmetrical multiprocessing SMP L2 : 8MB per card L3 : 36MB per processor card |
|  | Local and Remote GUI Administration interface |
|  | Have full range of diagnostics & Self Diagnostics Capabilities |
|  | Support Four standard, plus four optional internal disk storage |
| Memory | 32 GB 276-pin, DDR-2 SDRAM ECC Expendable 128GB |
| Disk Storage | Dual integrated channel Ultra320 SCSI controller |
|  | Equipped with 2 x 146 GB 15,000 RPM SAS Disk Drive up to 6 HDD with the same server, RIAD 1, 0 |
|  | IDE Slim line DVD-ROM Drive |
| I/O Adapters | Integrated Dual ported Ethernet 10/100/1000 Mbps controller Equipped with Three USB, Two system ports Two HMC( Hardware Management Console) GXT13P VGA Port Two RS232 port adapter Two 4GB Single-Port Fiber Channel PCI-X DDR Host Bus Adapter |

| I/O Slots | Two PCI-X (266 MHz DDR); Three PCI Express 8x |
| --- | --- |
|  | Upgradable up to eight I/O drawers (combination of 7311-D20 &/or 7314-G30) |
|  | All PCI Slots hot swappable |
|  | support PCI Extended error handling |
| Application | Install and run Latest J2se version Install & run the latest ver. of tomcat servlet container & ingress client side |
| Operating System | -Linux Red Hat Enterprise 5.3 and 6 with Red Hat License Renewal for Latest Power operating System. -UNIX AIX Support |
| Database | Support latest version of Ingres with Clustering. |
| Power Supply & Cooling | Dual Redundant AC Power Supply, 1700Watt Two hot swap power Supply Two hot-swap cooling fans |
| Cluster Software | With Red hat Linux on two server (database server) Ingres database |

- IBM total Storage DS5100 type(1818-51A)  Qty 1

IBM Total Storage DS5100

Description

Dual active, Dual, redundant 4Gbps RAID controllers with up to 8 GB of cache memory (4 GB per RAID controller).

Mirrored-enabled New lithium-ion battery backup protects data cache in each controller for at least 72 hours. Hot-swappable cache backup battery.

8 host ports—Fiber Channel (FC) Switched and FC Arbitrated Loop (FC-AL) standard, auto-sensing 1Gbps /2Gbps /4Gbps

4Gbps end to end solution design (Servers, HBA, SAN Switches, Storage Host Port and Disk Speed)

Hot-Spare Feature (Supports Global Hot Spare.), supporting multiple disk spears distributed across the SAN storage Expansions. The Hot-spear Disk able to be assigned to any Disk expansion Drawer to replace the filing Disk Unit.

Expandable up to 224 Drive

16 Host License Partition

Support up to 16 Disk drives per drawer

14 x 146.8 4GB/s FC 15K RPM HDD)Raw Capacity

Support Raid 0,0-1,5 and 10

Total Storage Capacity up to 100.8TB using 450GB FC Drive

1600MBps Bandwidth for High throughput applications

575,000 IOPS

GUI Hardware and software management to monitor perform and configure the Storage Box.

Redundant Hot-Swap Power supplies and Fan.

Support Multiple heterogeneous server and operating system support Windows , Linux, HP-UX , AIX & Solaris (Windows, AIX & Linux host kits Included in the Price)

Rack Mountable.

- IBM System Storage SAN24B-4 Express Fiber Switch  Qty 2

IBM System Storage SAN24B-4 Express

| Description |
| --- |
|  | 1U 19" packaging designed for rack-mount or table-top |
|  | Fibre Channel interface : E_Port, F_Port, FL_Port and M_Port |
|  | Protect existing 4, 2 and 1 Gbps infrastructure investment while positioning for future technologies |
|  | 24 ports 4GB per port |
|  | Dual fans, one power supply |
|  | Foundation for new infrastructure simplification and business continuity solutions for servers running Microsoft® Windows®, Unix®, Linux® and IBM AIX® and OS/400® operating systems |
|  | 4 Gbps SW SFP Transceiver 8-Pack |
|  | 8 X Fibre Cable LC/LC 5m multimode |
|  | Provides fast and easy replacement of optical transceivers with no tools required |
|  | Support for up to 8-port ISLs provides total bandwidth of 128 Gbps |
|  | Management Ethernet port |

- IBM total Storage TS3200 Tape Library

IBM System Storage TS3200 Tape Library

| Description |
| --- |
|  | Rack Mount |
|  | Equipped with two LTO 3 Fiber Drives (400/800GB) |
|  | Based on IBM LTO Technology 3rd Generation |
|  | 4GB Fiber Channel |
|  | Provide with path fail over for both control paths and data paths |
|  | 48 slot |
|  | 30x LTO 3 Data Cartridges and two cleaning cartridge |
|  | Remote management and web management |
|  | Up to 19.2TB(38.4TB with 2:1 compression) |
|  | Up to 800GB per cartridge compressed; 400 GB native per Tape Media |
|  | Average of 80 MB/s native transfer with LTO 3 |
|  | Support all major operating systems such as Linux , HP-UX, Solaris, AIX and windows |
|  | Dual Redundant Power supply & cooling Fan |

- Monitor console

| Monitor console | Description |
| --- | --- |
|  | 1U 15" Flat Panel Monitor Console Kit |
|  | IBM USB Travel Keyboard with UltraNav (mouse) |
|  | IBM 1x8 Console Switch |
|  | 2 x 3m Console Switch Cable (USB) |
|  | Kvm switch 1*8 |

- Server HP proliant  DL 360 G6   Qty =3 :

A:

| Server Model | HP proliant DL 360 G6 |
| --- | --- |
| Processor family | 2 Quad core Intel CPU E5530, 2.4 GHz |
| Number of processors | 2 |
| Processor core available | 6 or 4 or 2 |
| Storage | 600GBx2 SAS 2.5”,10K HDD drives and 72GBx2 SAS 2.5”,10K HDD drives |
| memory | 28 GB |
| Maximum memory | 192 GB |
| Memory slots | 18 DIMM slots |
| Memory type | PC3-10600R RDIMMs DDR3 or PC3-10600E UDIMMs DDR3 |
| Expansion slots | 2 |
| Network Controller | 2 NICs HP NC382i DP Multifunction Gigabit Server Adapters |
| Maximum drive bays | 4) SFF SAS/SATA/SSD (8) SFF SAS/SATA/SSD |
| Supported drives | Hot plug SFF SAS Hot plug SFF SATA |
| Storage Controller | (1) Smart Array P410i Integrated |
| Power Supply | Hot-Plug redundant power supply |
| Operating system | Windows server 2012 R2 Datacenter |

B:

| Server Model | HP proliant DL 360 G6 |
| --- | --- |
| Processor family | 2 Quad core Intel CPU E5530, 2.4 GHz |
| Number of processors | 2 |
| Processor core available | 6 or 4 or 2 |
| Storage | 72GBx4 SAS 2.5”,10K HDD drives |
| memory | 22 GB |
| Maximum memory | 192 GB |
| Memory slots | 18 DIMM slots |
| Memory type | PC3-10600R RDIMMs DDR3 or PC3-10600E UDIMMs DDR3 |
| Expansion slots | 2 |
| Network Controller | 2 NICs HP NC382i DP Multifunction Gigabit Server Adapters |
| Maximum drive bays | 4) SFF SAS/SATA/SSD (8) SFF SAS/SATA/SSD |
| Supported drives | Hot plug SFF SAS Hot plug SFF SATA |
| Storage Controller | (1) Smart Array P410i Integrated |
| Power Supply | Hot-Plug redundant power supply |
| Operating system | REDHAT 5 |

C:

| Server Model | HP proliant DL 360 G6 |
| --- | --- |
| Processor family | 2 Quad core Intel CPU E5530, 2.4 GHz |
| Number of processors | 2 |
| Processor core available | 6 or 4 or 2 |
| Storage | 300GBx2 SAS 2.5”,10K HDD drives and 600GB SAS 2.5”,10K HDD drives |
| memory | 28 GB |
| Maximum memory | 192 GB |
| Memory slots | 18 DIMM slots |
| Memory type | PC3-10600R RDIMMs DDR3 or PC3-10600E UDIMMs DDR3 |
| Expansion slots | 2 |
| Network Controller | 2 NICs HP NC382i DP Multifunction Gigabit Server Adapters |
| Maximum drive bays | 4) SFF SAS/SATA/SSD (8) SFF SAS/SATA/SSD |
| Supported drives | Hot plug SFF SAS Hot plug SFF SATA |
| Storage Controller | (1) Smart Array P410i Integrated |
| Power Supply | Hot-Plug redundant power supply |
| Operating system | Windows server 2012 R2 Datacenter |

- Netback-up Server:         Qty:1

| Server Model | IBM system x3400 |
| --- | --- |
| Processor family | 6 Intel(R) Xeon(R) CPU E5420 @ 2.50GHz |
| Number of processors | 4 |
| Storage | 146.6 GB |
| memory | 4GB |
| Memory slots | SLOT DIMM 12 DDR2 Synchronous |
| Operating system | Redhat linux |
| Power Supply | Hot-Plug redundant power supply |

- VERITAS NBU software support

Support includes installation,Re-installation,upgrade,pacthes,fixes,update to latest releases, and solving issues on Net-Backup software and configuring and integration with the existing tape library system.

- Required Licensing:

- VERITAS NBU  License Renewal  and Support for the following items:-

(1 Year License starting from 1-Jul-2017 for Customer Number:  2297649R) :-

| Item Instance Number | Product Name/Description | Quantity |
| --- | --- | --- |
| 49029704 | 13124-M2-23 ESSENTIAL 12 MONTHS RENEWAL FOR NETBACKUP OPT SHARED STORAGE OPT XPLAT 1 DRIVE ONPREMISE STANDARD PERPETUAL LICENSE ACD | 2 |
| 49029694 | 13102-M2-23 ESSENTIAL 12 MONTHS RENEWAL FOR NETBACKUP CLIENT APPLICATION AND DB PACK WLS 1 SERVER HARDWARE TIER 2 ONPREMISE STANDARD PERPETUAL LICENSE ACD | 2 |
| 49029699 | 14731-M2-23 ESSENTIAL 12 MONTHS RENEWAL FOR NETBACKUP ENT CLIENT WLS 1 SERVER HARDWARE TIER 2 ONPREMISE STANDARD PERPETUAL LICENSE ACD | 2 |
| 49029703 | 12250-M2-23 ESSENTIAL 12 MONTHS RENEWAL FOR NETBACKUP ENT SERVER WLS 1 SERVER HARDWARE TIER 2 ONPREMISE STANDARD PERPETUAL LICENSE ACD | 1 |
| 49029700 | 11142-M2-23 ESSENTIAL 12 MONTHS RENEWAL FOR NETBACKUP OPT LIBRARY BASED TAPE DRIVE XPLAT 1 DRIVE ONPREMISE STANDARD PERPETUAL LICENSE ACD | 2 |

- RedHat Licenses

| item | License | Qtty | End Date |
| --- | --- | --- | --- |
| 1 | RedHat Subscriptions : - High-Availability (1-2 sockets) | 4 | 17/04/2017 |
| 2 | Red Hat Enterprise Linux Academic Server, Self-support (16 sockets) (Up to 1 guest) with Smart Management | 8 | 17/04/2017 |
| 3 | RedHat 6 Enterprise Linux for Virtual Datacenters(SKU RH00002), 2 sockets ,unlimited virtual, no physical Standard Subscription/1 year | (2) 1 New License 1 Renew of an existing one | 23/07/2017 |

•Licenses must be renewed after end date for each of the required current license.

شروط خاصة :

      - تقدم الأسعار بالدينار الأردني شاملة جميع أنواع الضرائب والرسوم الجمركية وشاملة ضريبة المبيعات لكل بند من البنود المذكورة في الجداول أعلاه.

      - الجامعة غير مقيدة بأقل الأسعار، ولها الحق في تجزئة العطاء أو إلغائه كلياً أو جزئياً حسب ما تقتضيه المصلحة، دون أن يكون للمناقصين حق الاعتراض أو المطالبة بأية خسارة أو ضرر ناتج عن ذلك.

      - مدة هذا العطاء عام واحد من تاريخ التوقيع على قرار الإحالة وعقد الصيانة والعطاء قابل للتجديد بالشروط ذاتها واتفاق الطرفين.

      - طريقة الدفع : تكون طريقة الدفع على دفعتين متأخرتين بواقع دفعة في نهاية كل ستة أشهر، وذلك من خلال تقرير فني يبين فيه مدى التزام المتعهد بشروط قرار الإحالة وعقد الصيانة تقدمه الجهة المعنية بمتابعة تنفيذ العطاء (مركز الحاسوب) ولا يستحق المتعهد الدفعة في حال مخالفته ولا يحق له الاعتراض على ذلك.

      - يلتزم المتعهد بصيانة الأجهزة في هذا العطاء وإبقائها جاهزة للعمل (عاملة).

      - يشمل المبلغ جميع قطع الغيار اللازمة وأجور تركيبها وأتعاب أو أجور المتعهد، والتنقل والشحن والدعم الفني للبرمجيات.

      - يقوم المتعهد بإجراء أعمال الصيانة اللازمة للأجهزة عند الطلب والصيانة الوقائية الدورية كل ثلاثة أشهر، ويشترط في ذلك أن لا يقوم المتعهد بأعمال الصيانة إلا بموعد مسبق تحدده الجامعة.

      - للجامعة الحق باستدعاء المتعهد هاتفياً أو بالفاكس أو البريد الإلكتروني (على أن يكون الهاتف والبريد معتمداً رسمياً لغايات التبليغ عن الأعطال) وتبليغه بالأعطال الفنية والطلب منه القيام بأعمال الصيانة اللازمة، ويلتزم المتعهد بالاستجابة لهذا الاتصال خلال مدة لا تزيد عن (3) ثلاث ساعات عمل من لحظة تبليغه، ويكون هذا التبليغ على مدار الساعة بما فيها أيام العطل.

      - يلتزم المتعهد وعلى نفقته بتوفير قطع الغيار اللازمة لبقاء الأجهزة في وضع تشغيلي طبيعي، وتتم إجراءات الإصلاح والصيانة كالتالي:

يقوم المتعهد بإصلاح العطل خلال (8) ثماني ساعات من وقت التبليغ، وإذا لم يتمكن من الإصلاح يقوم بتوفير جهاز بديل مكافئ أو أفضل من حيث الجودة والمواصفات الفنية خلال فترة (24) ساعة من تاريخ التبليغ لحين إصلاح العطل. وفي حال عدم تمكن المتعهد من إصلاح العطل أو توفير جهاز بديل خلال (24) ساعة، فإنه يحق للجامعة القيام بالأعمال اللازمة لإصلاح العطل أو شراء أجهزة أو برمجيات على نفقة المتعهد مضافاً إليها (15%) كمصاريف إدارية، وبخلاف ذلك خصم ما قيمته (2%) من قيمة الإحالة الإجمالية عن كل يوم تأخير في إصلاح العطل، بناءً على تقرير فني من الجهة المعنية (مركز الحاسوب).

      - تتم أعمال الصيانة باستبدال أو إصلاح القطع المعطلة لحل المشاكل حسب ما تقتضيه الظروف، وتحت إشراف الجامعة، وتعتبر القطع التالفة المستبدلة ملكاً للمتعهد ولا يحق للجامعة المطالبة بها.

      - تقوم الجامعة بالإشراف على الأعمال التي يقوم بها المتعهد ويقدم المتعهد تقارير الصيانة للجامعة بعد انتهاء كل زيارة للموقع لغايات اعتمادها.

      - لا يسمح لطرف ثالث بإجراء عمليات الصيانة، وكذلك لا يجوز استخدام مواد أو قطع غير التي توصي بها الشركة الصانعة، إلا بموافقة الجامعة.

      - في حال الأعطال الناتجة عن الظروف القاهرة كالحريق والحروب والكوارث الطبيعية والإضرابات وما شابه ذلك أو كان بحكمها، يقوم المتعهد بأعمال الصيانة اللازمة على نفقة الجامعة بعد الاتفاق معها على الكلفة.

      - في حال الأعطال الناتجة بفعل القوارض يقوم المتعهد بأعمال الصيانة اللازمة وعلى نفقته.

      - تشمل هذه الاتفاقية فك ونقل وإعادة تركيب الأجهزة.

      - تشمل هذه الاتفاقية تحديث (Upgrade) إصدارات (Releases) أنظمة التشغيل والبرمجيات المساعدة، وكذلك دعم هذه الأنظمة وتحميلها (Installation) أو إعادة تحميلها (Reinstallation).